## Slide 1: PRODML Distributed Acoustic Sensing (DAS)
Worked Example Tutorial (v1)
For PRODML v2.0

## Slide 2: Overview
This presentation deck includes slides for the DAS worked example. For more information, see the PRODML Technical Usage Guide, which is included in the zip file when you download PRODML from the Energistics website.

## Slide 3: DAS Fundamentals

## Slide 4: DAS High-Level Block Diagram
DAS Interrogator Unit
DAS
Raw
DAS
Processed
DAS
Processing
DAS data repository
Raw data
Terabytes
Processed data frequency band, spectrum, … Gigabytes, Mbytes
Well
Fiber Optic Cable
Application 1
Application 2
Application 3

## Slide 5: DAS High-Level Data Transfer
Raw data storage
Extracted data
Raw data transfer
Main tasks
Planning and proposal
Project start up
Raw data collection
Near realtime extraction and processing
Extracted data visualization
Transfer of calibrated raw data for further processing
Storage and transfer of real-time / near real-time extracted data for further data processing
Main tasks
Data processing
Data analysis
Data integration and interpretation
Archive relevant data
Destroy irrelevant data
Field
Office
DAS data exchange
Extracted data storage and transfer

## Slide 6: DAS Nomenclature
Decimated Output Data (Decimation Factor 4)
Measurement Start Time
Output Data Rate (=Number of Scans /Traces per second)
Surface fiber Loci 0-4
DAS
Interrogation Unit
N
0 1 2 3 4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
…
0 1 2 3 4 5 6 7 8
Time
Decimated Output Data (Decimation Factor 4)
Fiber End
Well Head
fiber length corresponding to a Locus
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Time Series for one Locus
Start Locus Index
(for measurement)
Number of Loci = 17 (8 - 24) recorded
Downhole fiber
Loci 5 - N
Spatial Sampling Interval
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
N
Locus Index
0
1
2
3
4
Locus Index
Surface fiber Loci 0-4
Casing
Perforated
Casing
section
Production
packer
Production
tubing

## Slide 7: DAS Detailed Data Transfer (1 of 2)
Raw data storage
Planning and proposal
Raw data collection
Data quality assurance
Near real time data extraction / processing
Extracted data visualisation
Project start up
Review application requirements
Review existing datasets
Determine if DAS acquisition would create additional value
Data transfer
DAS data life cycle
Fiber deployment (if not installed)
Specify / agree on DAS data acquisition specifications
Data acquisition hardware mobilisation
Raw DAS data from interrogator unit
Depth calibration
Time calibration (if required)
Sensor calibration (if required)
Meta data population / instantiation
On site storage of calibrated acoustic traces (in external storage medium)
Transfer of calibrated raw data for further processing
Real-time / near real-time data extraction (e.g.: Real time Frequency band extraction)
Data reduction
Extracted data storage and transfer
Storage and transfer of real-time / near real-time extracted data for further data processing
Visualise relevant information for real time / near real time decisions at well site support
Field
Office
DAS data exchange

## Slide 8: DAS Detailed Data Transfer (2 of 2)
Data processing
Data integration and interpretation
Data pre-processing
Data analysis
Repurpose and reuse
Data transfer
Archive relevant data
End of project
Transfer of calibrated raw data for further processing
Extracted data storage and transfer
Storage and transfer of real-time / near real-time extracted data for further data processing
Further acoustic data processing
Manage raw data sets
Process and analyse raw data
Repurpose data if required and reprocess
Data destroy
Select data traces to be archived as per company retention policy or for future R&D purposes
Destroy data that reached end-of-retention-period or unwanted data
Integration of acoustic data with other data as required
Data and knowledge sharing
Field
Office
DAS data exchange

## Slide 9
Sine wave exciting a channel displayed as a wiggle plot
Sine wave exciting a channel displayed using false colour for amplitude
Time
Fiber Distance
Fiber Distance
Fiber Distance
Fiber Distance
Time
DAS Raw data
A
Frequency band that includes the frequency of the sine wave
Frequency band that excludes the frequency of the sine wave
Time
DAS Frequency Band data
B
DAS Spectrum data
Spectrogram of the single channel including the sine wave
Time
Frequency
C
DAS Data Types

## Slide 10: Distributed Acoustic Sensing (DAS)
How does it work (1)
Coherent OTDR
  Coherent pulse propagates along the fiber
  Tiny density fluctuations frozen into fiber during manufacture → act as scatter sites
  Scattered light is captured and travels back toward detector
  Detection time directly maps to location
  Detected intensity is a function of the local properties of the waveguide

## Slide 11: “Still” of Back Scattering

## Slide 12: Distributed Acoustic Sensing (DAS)
How does it work (2)
Coherent scatter pattern remains constant on successive pings
Vibration from an acoustic source modulates the fiber and hence the scatter pattern
A history of the nature of acoustic source as a function of position may be determined

## Slide 13: “Still” of Scattering Influenced by Sound

## Slide 14: DAS Data Model

## Slide 15: DAS Conceptual Model for Raw and Processed Arrays

## Slide 16: DAS Possible HDF5 Array Configurations (1/2)
Hybrid
File 1
File 2
1
2
Processed separate file
File 1..
File n+1
1
2
Processed with own raw
File 1
File 2
1
2
File n
1
2
Arrays
RawDataPart
FbeData 1
SpectraData
RawTracesTime
SpectraDataTime
FbeData 2
FbeDataTime

## Slide 17: DAS Possible HDF5 Array Configurations (2/2)
Raw Only
File 1 …
File n
Processed Only
File 1
1
2
Arrays
RawDataPart
FbeData 1
SpectraData
RawTracesTime
SpectraDataTime
FbeData 2
FbeDataTime

## Slide 18: DAS Worked Example
Raw
Fbe 1
..
..
Processed
Spectra 1
..
..
Array Data
Raw
Fbe 1
Spectra 1
Arrays
RawDataPart
FbeData 1
SpectraData
RawTracesTime
SpectraDataTime
FbeData 2
FbeDataTime
HDF5 Arrays
File 1
File 2
1
2
Data Acquired and Processed

## Slide 19: EPC: Energistics Packaging Conventions

## Slide 20
(or other Energistics standard)
DAS Acquisition
Optical Path
Raw Data
Instrument Box
Formatted using:
HDF5
EPC
EPC
Title : mytitle
Identifier : myUuidUrn
Creator : Energistics
…
Processed Data: FBE
Processed Data: FBE
Processed Data: FBE
Raw DataY
Raw Data
Processed Data: Spectrum
Processed Data: Spectrum
Processed Data: Spectrum
(or other Energistics standard)
All measurement data is stored externally to the EPC file, using HDF5, which is technology especially designed to handle huge data sets.
Notes: Container ship photo from wikipedia : http://fr.wikipedia.org/wiki/Fichier:CMA_CGM_Marco_Polo_arriving_Port_of_Hamburg_-_16._01._2014.jpg
Licence : Creative Commons paternité – partage à l’identique 3.0 (non transposée)

## Slide 21: Data Package is: EPC Container for XMLs, plus External HDF5 files with arrays of numbers
One EPC, 2 HDF5 files
H5 files contain data arrays
and are called External Parts
XML Describes whole data set
XML Provides reference to External Part Reference (one per HDF5 file)
EPC is a zip file container
For each of the XML files, provides relationships to other files including external HDF5 files
EPC File
Rels folder
Notes: obj_Acquisition_uuid_xml: This XML describe the whole data set including parameters of Acquisition; Raw Data; Custom Data; Calibration and Processed Data, as well as their external references (if any)

## Slide 22
How Extenral Pat Reference Works
EPC External Part Reference File
EPC File
DAS Acquisition File
External Part Reference (EPR) is a proxy for HDF5 File
Path in HDF5 File for an array
EPR for the HDF5 file containing the array

## Slide 23
Summary
From Das Acquisition the Raw can be split into 1..* arrays
Each split part has 1 EPC External Refs which allow navigation to the HDF5 file.
Each split part has its path within that file.
How External Parts Work
Part 2 - Rels files
This file (EPC External Part Ref. XML) has relationship to Das Acquisition and to one named external HDF5
Summary
From Das Acquisition the Raw can be split into 1..* arrays
Each split part has 1 EPC External Refs which allow navigation to the HDF5 file.
Each split part has its path within that file.
Rels folder with .rels files
This file (Das Acquisition XML) has relationship to
2 External Part Ref. files
+ optical path + instr box

## Slide 24
DasAcquisition File
1st part
Part1.h5
Value arrays split across multiple HDF5 files showing path in HDF5 file and indices
2nd part
Part2.h5
Rels file for this ext part ref shows HDF5 file name

## Slide 25
Keeping files associated in both directions
Every HDF5 Acquisition Group has attribute Acquisition ID. This is the uuid of the DAS Acquistion xml of which it is the data.
DAS Acquisition xml
HDF5 file
HDF5 file
Ext Part Ref file
Every HDF5 file has an attribute uuid. This should be used to store the uuid of the External Part Reference xml of which it is the data.

## Slide 26: DAS Data Arrays

## Slide 27: DAS raw data array values: 101 loci (horizontal 0-100), 37 samples (vertical 0-36) in h5 file part1.h5
Part2.h5 has the same loci and the samples continue in sequence, 38 samples (37-75)

## Slide 28: DAS raw trace times array and attributes in h5 file part1.h5

## Slide 29: Processed Data

## Slide 30: DAS FBE attributes h5 file part1.h5

## Slide 31: DAS FBE attributes and array values and for frequency band FbeData[1] in h5 file part1.h5

## Slide 32: DAS Spectra data attributes

## Slide 33: DAS FFT spectra for the spectra data array in h5 sample file part1.h5

## Slide 34: Spectra data time array and attributes in H5 sample file part1.h5

## Slide 35: Optical Path

## Slide 36: Optical Path
Describes all components through which light passes (fiber + other components)
Can span more than one wellbore
Provides mapping from path length to position in a facility (wellbore or pipeline)
Records defects that impact measurements
Conveyance
Shows changes versus time

## Slide 37: Optical Path Components

## Slide 38: Optical Path can span multiple facilities

## Slide 39: Fiber may be linear or “folded” along the facility (well, pipeline etc.) being measured

## Slide 40: Optical Path Connectivity Representation
fiber segment 1
connector 1
fiber segment 2
PRODML Network Representation
Network (represents the whole optical path)
Unit (represents each component)
Port (place where component connects)
Node (virtual point of connection)
Port 1
Port 2
Port 1
Port 2
Port 1
Port 2
Node a
Node b
Node…
Ins. Box port
First component (and terminator*) can name Instrument Box port connected
Each unit has 2 ports
Ports with a common “connected Node” are connected
Etc.
Section illustrated
Each component is a “unit”
* - for double ended systems looped back to box

## Slide 41: Fiber Facility Mapping links path distance to facility length, enabling facility “logs” to be made

## Slide 42: Fiber Defects recorded along Optical Path (Example data from OTDR test)

## Slide 43: Optical Path may record changes over time: use of Inventory and Network allows for this

## Slide 44: Simple Optical Path Example

## Slide 45: Simple Optical Path Example – 101 loci measurement

## Slide 46: Simple Optical Path Example – 101 Loci Measured - Calibration

## Slide 47: Optical Path example network showing connectivity

## Slide 48: Instrument Box